Origin of the Zero-Field Splitting in Mononuclear Octahedral MnIV complexes:

A Combined Experimental and Theoretical Investigation

Zlatar, M.; Gruden, M. (U. of Belgrade, Serbia); Vassilyeva, O.; Buvaylo, E.A. (U. of Kyiv, Ukraine); Ponomaryov, A.N.; Zvyagin, S.A.; Wosnitza,  J. (Dresden High Magnetic Field Laboratory, Germany); Krzystek, J. (NHMFL); Garcia-Fernandez, P. (U. of Cantabria, Spain) and Duboc, C. (U. Grenoble Alpes, France)

Introduction

The aim of this work was to determine and understand the origin of the electronic properties of MnIV complexes, especially the zero-field splitting (ZFS), through a combined experimental and theoretical investigation on five mononuclear MnIV compounds, with various coordination spheres (N6, N3O3, N2O4 in both trans (trans-N2O4) and cis configurations (cis-N2O4) and O4S2). In particular, high-frequency and -field EPR (HFEPR) spectroscopy was applied to determine the ZFS parameters of two of these compounds, MnLtrans-N2O4 and MnLO4S2.

Experimental

The experiments conducted at NHMFL used Virginia Diodes Inc. sub-THz wave sources and a 15/17-T SC magnet. The MnLO4S2 sample was ground and pressed into a pellet with n-eicosane because of a strong torquing effect observed in neat powder. The electrostatic powder of MnLtrans-N2O4 was immobilized in an n-eicosane mull.

Results and Discussion

While the X- and Q-band EPR spectra of MnLtrans-N2O4 were uninformative, the accurate values of the ZFS parameters were determined thanks to analysis of the HFEPR spectra: D = (0.997(6) cm(1, E = (0.054(3) cm(1, E/D = 0.054 (see the two-dimensional field/frequency map in Fig. 1). Regarding the complex MnLO4S2, previous X-band EPR experiments found ZFS to be of moderate magnitude (D = +0.47 cm(1, E/D = 0.09).1 Unexpectedly, the HFEPR investigation lead to a very different set of parameters: D = +2.289(5) cm(1, E = +0.323(4) cm(1 E/D = 0.141, the magnitude of D being the largest ever measured for a MnIV complex. This work demonstrates that estimating the ZFS in absence of high frequency/field limit is risky at best. Specifically, ZFS values for MnIV resulting from low-frequency studies should thus be taken with caution, but the problem is of more general nature and concerns a larger number of high-spin (S > 1/2) Kramers (half-integer spin number) metal ions (non-Kramers ions are typically ‘EPR-silent’ in the same conditions).

Conclusions

The experiments carried out at the NHMFL were part of a combined experimental and theoretical study that defined and quantified the different contributions to the ZFS. On the experimental aspect, it highlights the fact that contrary to a common belief, ZFS in MnIV complexes can be of the same order of magnitude as that in MnIII.

Acknowledgements

A portion of this work was performed at the National High Magnetic Field Laboratory, which is supported by National Science Foundation Cooperative Agreement No. DMR-1157490 and the State of Florida. This work was supported by Deutsche Forschungsgemeinschaft (DFG, Germany), the European Magnetic Field Laboratory (EMFL), the French National Agency for Research n° ANR-09-JCJC-0087, Labex arcane (ANR-11-LABX-003) and IR-RPE CNRS 3443, COST Action CM1305 ECOSTBio (COST-STSM-CM1305-25068).

References

[1]	Paine, T.K., et al., Dalton Trans., 3136 (2003).

# Text boxes

Fig. 1. Field vs. frequency map of resonances observed in MnLtrans-N2O4 at 4.5 ( 7 K. The squares are experimental HFEPR resonances while the curves were simulated using the parameters given in the text. Color caption: red for B0||x, blue for B0||y; black for B0|| z and green for off-axis turning points.