## Slide 1
The brain is the only part of the body without a lymphatic system to clear metabolic waste. Recent evidence suggests brain clearance of waste may be accomplished in the annular spaces around cerebral blood vessels, called perivascular spaces (PVS), through which cerebrospinal fluid (CSF) is transported.
In this work, MagLab users reconstructed the PVS network in the whole rat brain using the MagLab’s 17.6T, 89mm bore MRI system to measure contrast enhanced three-dimensional images of the PVS with a resolution that is two orders of magnitude higher than previously reported.
An MR visible tracer (Gd-albumin) was infused in vivo into the CSF-filled lateral ventricle followed by ex vivo high-resolution MR imaging (Figure 1). Tracer distribution patterns were reconstructed using a tube-following algorithm, since the PVS surround the blood vessels. This results in a more complete visualization of the PVS network in the brain (bright regions in the bottom image) to elucidate both PVS uptake and clearance pathways. PVS connections were highlighted repeatedly across several brains, and new PVS connections between ventricles and different parts of the functional tissue of the brain were revealed. This suggests a role for the ventricles as a source or sink for metabolites in the brain.
Facilities and instrumentation used: AMRIS Facility & 17.6 T, 89 mm bore MRI system.
Citation: Magdoom, K.N.; Brown, A.; Rey, J.; Mareci, T.H.; King, M.A.; Sarntinoranont, M., MRI of Whole Rat Brain Perivascular Network Reveals Role for Ventricles in Brain Waste Clearance, Nature Scientific Reports, 9, 11480 (2019) doi.org/10.1038/s41598-019-44938-1
High Magnetic Field MRI Evidences Pathways
for Metabolic Brain Waste Clearance
Kulam Najmudeen Magdoom1, Alec Brown1, Julian Rey1, Thomas H. Mareci2,
Michael A. King3 & Malisa Sarntinoranont1
1. University of Florida, 2. NHMFL, 3. Veterans Administration;
Funding: G.S. Boebinger (NSF DMR-1157490); K. Magdoom (Chiari & Syringomyelia Foundation)
(Top) Cartoon of side view and (bottom) actual MRI cross-section of the mouse brain, showing injection site for the contrast agent (green arrows) and circulation pathways in the brain. MRI at 17.6T shows that the Gd-Albumin contrast agent (red in bottom image) circulates through the ventricles and perivascular spaces of the brain.

## Slide 2
What is the finding?
MRI can provide exquisite visualization of the brain with the resolution necessary to visualize the small annular spaces around cerebral blood vessels (red in Figure 1) known as the peri-vascular network (PVS). This enabled MagLab users to find connections between the ventricles and the functional tissue of the brain through the PVS.
Why is this important?
This finding demonstrates a possible pathway for metabolic waste clearance from the brain with the ventricles providing a source or sink for metabolites. This may be related to the daily requirement for sleep, since recent studies indicate that the perivascular network dilates during sleep, enabling enhanced flow.
Why did this research need the Maglab?
At present, this research can only be performed at the MagLab AMRIS Facility because it requires the use of a high magnetic field (17.6 T), wide bore (89 mm) imaging spectrometer. This instrument was specifically designed for high resolution spectroscopy and imaging (combining high magnetic field, strong gradients, unique MRI coils, and high field homogeneity) and provides the sensitivity necessary for detecting contrast enhanced MR at the high resolution needed to visualize the three dimensional PVS network within an intact brain.
Figure: A contrast agent, Gd-Albumin (red), was injected via the path indicated by the green arrow. Contrast-enhanced MRI enables visualization of the perivascular system (PVS) using a tube-following algorithm, since the PVS surrounds blood vessels in the brain. This allowed the identification of important PVS connections between the ventricles and functional tissue of the brain. The data suggest an important role for the brain’s ventricles as a source or sink of metabolites in the brain.
Facilities and instrumentation used: AMRIS Facility & 17.6 T, 89 mm bore MRI system.
Citation: Magdoom, K.N.; Brown, A.; Rey, J.; Mareci, T.H.; King, M.A.; Sarntinoranont, M., MRI of Whole Rat Brain Perivascular Network Reveals Role for Ventricles in Brain Waste Clearance, Nature Scientific Reports, 9, 11480 (2019) doi.org/10.1038/s41598-019-44938-1
High Magnetic Field MRI Evidences Pathways
for Metabolic Brain Waste Clearance
Kulam Najmudeen Magdoom1, Alec Brown1, Julian Rey1, Thomas H. Mareci2,
Michael A. King3 & Malisa Sarntinoranont1
1. University of Florida, 2. NHMFL, 3. Veterans Administration;
Funding: G.S. Boebinger (NSF DMR-1157490); K. Magdoom (Chiari & Syringomyelia Foundation)